## Slide 1: GPPU Experiment P1 (2025)
2026/2/24 – 2/26
RCNS I-03
Name:
E-mail:
Finish date/time : 2026/2/ :

## Slide 2: Rule
Do not rewrite program codes used in your laboratory or written by your senior students.
Please write your code by yourself or using the base codes in the laptop PC.

## Slide 3
e-
θ
Eg
E’g
E’e
me
1.1 Considering Compton scattering, show E’g and E’e using Eg, me and q .
1.2 Calculate E’g and E’e when Eg =1.0[MeV], me =0.511 [MeV/c2] and q =180o.

## Slide 4
Calculation page

## Slide 5
70cm
30cm
20cm
90cm
50cm
40cm
x
z
2.1 Basic detector design z-x view
(@ y=0)

## Slide 6
70cm
30cm
20cm
70cm
30cm
20cm
x
y
1 LeadShilding (G4_Pb)
2 CupperShilding (G4_Cu)
3 MeasurementArea
(G4_Air)
2.2 Basic detector design y-x view (@ z=0)

## Slide 7
3 Ge detector design
Al case (G4_Al)
thickness 0.8mm
Φ80mm
Vacuum case
(G4Galactic)
100mm
Φ75mm
5mm
80mm
Kapton window
(G4_Kapton)
thickness 0.1mm
Φ70mm
Cu case (G4_Cu)
thickness 0.8mm
Ge crystal
(G4_Ge)
Vacuum Space
(G4Galactic)
60mm
45mm
Φ8mm
Vacuum Core
(G4Galactic)
z

## Slide 9
3.2 Ge detector Position
x
z
x
y
Set top-center part of Al case to (0,0,0)

## Slide 10
4 Check Geometry using geantino
4.1 Check overlap
[Past your output]

## Slide 11
[Past your screen capture of Qt viewer]

## Slide 12
4.2 Show trajectories output of running geantino from position (0,0,490mm) and direction (0,0,-1). [Past your output /tracking/verbose 1] Check crossing positions of each geometrical elements are same as your expectations.
[Past your output]

## Slide 13
4.3 Show trajectories output of running geantino from position (0,10mm,490mm) and direction (0,0,-1). Check crossing positions of each geometrical elements are same as your expectations.
[Past your output]

## Slide 14
5.1 Activate Ge detector as a sensitive detector and record the energy deposition of each events and primary vertex information into root/csv file with tuple format .
Tuple formant
Name : Edep
0th column : Event number (integer)
1st column : Total energy deposit in Ge crystal (double)
2nd column : Primary vertex position x [mm] (double)
3rd column : Primary vertex position y [mm] (double)
4th column : Primary vertex position z [mm] (double)
5th column : Primary particle direction vector x (double)
6th column : Primary particle direction vector y (double)
7th column : Primary particle direction vector z (double)

## Slide 15
5.2 Generate 1000000 event of 1.0 MeV gamma position(0,0,10mm) and direction (0,0,1) . Make a histogram of energy deposition in Ge crystal and calculate the efficiency of detecting full energy deposition (gamma events shown as 1.0 MeV).
[Past your macro file]

## Slide 16
[Figure of Total energy deposit in Ge crystal ]
Detection efficiency of 1 MeV gamma event: ± [stat.]

## Slide 17
5.3 Generate 1000000 event of 1.0 MeV gamma position(0,0,10mm) and uniformed direction . Make a histogram of energy deposition in Ge crystal and calculate the efficiency of detecting full energy deposition (gamma events shown as 1.0 MeV). Make figures of primary particle directions (f and cosq distribution )
[Past your macro file]

## Slide 18
[Figure of Total energy deposit in Ge crystal ]
Detection efficiency of 1 MeV gamma event: ± [stat.]

## Slide 19
[f distribution of primary particle direction vector figure]

## Slide 20
[cosq distribution of primary particle direction vector figure]

## Slide 21
5.4 Do 5.2 as different gamma energies [0.25MeV, 0.5MeV, 0.75MeV, 1.25MeV, 1.5MeV,2.0MeV,2.5MeV]. Make histograms of each energies and calculate detection efficiency. Make table and figure of detection efficiency as a function of gamma energy.
Gamma Energy | Detection Efficiency (w/ stat. error)
0.25 | ±
0.5 | ±
0.75 | ±
1.0 | ±
1.25 | ±
1.5 | ±
2.0 | ±
2.5 | ±

## Slide 22
0.25MeV

## Slide 23
0.5MeV

## Slide 24
0.75MeV

## Slide 25
1.25MeV

## Slide 26
1.5MeV

## Slide 27
2.0MeV

## Slide 28
2.5MeV
Add comment for each peaks and edges shown in this figure

## Slide 29
Energy vs Detection efficiency
Add comments

## Slide 30
6. Extra
6.1 Set cupper square plate xwidth=20mm, ywidth=20mm, zwidth=5mm on the Ge detector top-center.
Check overlaps.
Al case (G4_Al)
thickness 0.8mm
Vacuum case
(G4Galactic)
Kapton window
(G4_Kapton)
thickness 0.1mm
Cu case (G4_Cu)
thickness 0.8mm
Ge crystal
(G4_Ge)
Vacuum Space
(G4Galactic)
Vacuum Core
(G4Galactic)
Cu plate

## Slide 31
6.2 Add record the mean energy deposition point of each event into root/csv file with tuple format .
Tuple formant
Name : Edep
0th column : Event number (integer)
1st column : Total energy deposit in Ge crystal (double)
2nd column : Primary vertex position x [mm] (double)
3rd column : Primary vertex position y [mm] (double)
4th column : Primary vertex position z [mm] (double)
5th column : Primary particle direction vector x (double)
6th column : Primary particle direction vector y (double)
7th column : Primary particle direction vector z (double)
8th column : Mean energy deposition point x [mm] (double)
9th column : Mean energy deposition point y [mm] (double)
10th column : Mean energy deposition point z [mm] (double)
Hint: Check case and fill dummy values at that case.

## Slide 32
6.3 Generate 1000000 event of 1.0 MeV gamma inside the cupper plate uniformly and uniformed direction . Make a histogram of energy deposition in Ge crystal and calculate the efficiency of detecting full energy deposition (gamma events shown as 1.0 MeV). Make figure of primary vertex positions and mean energy deposit positions.
[Past your macro file]

## Slide 33
[Figure of Total energy deposit in Ge crystal ]
Detection efficiency of 1 MeV gamma event: ± [stat.]

## Slide 34
[Figure of Primary Positions ]

## Slide 35
[Figure of Mean energy deposit Positions ]

## Slide 36
6.4 Generate 1000000 event of 1.0 MeV gamma from the cupper plate surface uniformly and uniformed direction . Make a histogram of energy deposition in Ge crystal and calculate the efficiency of detecting full energy deposition (gamma events shown as 1.0 MeV). Make figure of primary vertex positions and mean energy deposit positions
[Past your macro file]

## Slide 37
[Figure of Total energy deposit in Ge crystal ]
Detection efficiency of 1 MeV gamma event: ± [stat.]

## Slide 38
[Figure of Primary Positions ]

## Slide 39
[Figure of Mean energy deposit Positions ]

## Slide 40
6.5 Describe the difference of observed energy spectra between from inside the material and surface. Describe how these spectra can be distinguished?

## Slide 41
Appendix. Precise Ge detector